## Slide 1: Renesas Synergy platform ™ security built IN
Nick mori
Renesas Electronics corporation
Broad based solution b.U. , synergy platform div.
1/8/2018

## Slide 2: AGENDA
Understanding IoT Security Requirements
Solving IoT Security with Synergy
Synergy platform resources
Secure Level Planning
Secure Boot Loader Reference Project
Implementation plan
Secure Connectivity
Summary

## Slide 3
Understanding security
requirements

## Slide 4: Critical components of IoT security
Employs cryptography to limit access to information
Confidentiality
Assures platform is trustworthy and data is accurate
Integrity
Guarantees reliable performance under all conditions
Availability
Availability
Integrity
Confidentiality

## Slide 5: Focused Security Challenges for IoT
Protect Data
In Flight & At Rest
Privacy
Confidentiality
Enable Big Data
Create Robust Foundations
Root of Trust
Identity
Authentication
Authorisation
Protect Intellectual Property
IP Theft
Cloning
Over-building
Separate Critical
Functions
Protected Mode
Fail Safe
Secure Services
Manage Device Lifecycle
Lifetime Support
Critical Updates
Feature Enable
Confidentiality
Integrity
Availability

## Slide 6
Solving IoT Security challenges
using Synergy

## Slide 7: Synergy Core Security
Functions |  |  | Confidentiality | Integrity | Availability
Key Protection / Storage / Isolation |  |  |  |  | 
Cryptographic Services | True Random Number Generator |  |  |  | 
 | Ciphers | Symmetrical |  |  | 
 |  | Asymmetrical |  |  | 
 | Hash |  |  |  | 
Certificates / Chain of Trust |  |  |  |  | 
Secure Boot / Remote Firmware Update |  |  |  |  | 
Device Lifecycle Management |  |  |  |  | 
Data Protection (Key and data wrapping) |  |  |  |  | 
Secure Communication (e.g. TLS, MQTT) |  |  |  |  | 
Core Security
Advanced
Security

## Slide 8
Synergy platform resources

## Slide 9: MCU Hardware Security Features
Function |  |  |  | 
Secure Crypto Engine (SCE) Performance Acceleration NIST CAVP (Cryptographic Algorithm Verification Program) certifications in process Low Power Small firmware memory footprint Key isolation / wrapping1 |  |  |  Symmetrical encryption only | 
Secure Memory (Security MPU2) Sensitive code and data isolated in a separate domain |  |  |  | 3
One-Time Programmable Memory (FAW4) Allows code (e.g. boot code) and data (e.g. root keys, configurations) to be protected against being changed. |  |  |  | 
Limited JTAG access |  |  |  | 
1Keys are encrypted with a key unique to each MCU, so they are only accessible within the crypto module on a particular MCU
2Memory Protection Unit – Secure memory isolated from non-secure memory at the hardware level
3 S124 does not support Security MPU
4Flash Access Window – After initialization, only certain portions of flash memory can be written (i.e. initialized data can be locked for the product lifetime)
Notes: TSIP
  Performance: Hardware acceleration is provided for all cryptographic features that are available on that SKU. This results in improved price/performance/power consumption. This can have a significant impact on communications (TLS) efficiency. It will likely also improve boot and application flash update performance.
  Key Security: Keys can be wrapped so they are never exposed outside the crypto module and cannot be stolen from the device as they will only work on the same MCU. (i.e. No “dead copy”);
Secure Memory
  The bulk of the application is typically non-secure. Keys are typically stored in a secure portion of the memory.
  Any code that accesses those keys (or wrapped keys) and controls access to the use of those keys is also stored in a secure portion of the memory
  Never put the entire app in secure memory as you want to reduce the “attack surface”. For example if somebody hacks into the TCP/IP stack or the protocol of the TLS stack, they won’t have access to the keys.
OTP Memory: Typically used during manufacturing where the secure boot loader and associated data (e.g. OEM Identity keys) are secure against being modified.
Soft PUF Option address shortly below

## Slide 10: Synergy hardware cryptography features
Functions |  | S7 | S5 | S3 | S1
RSA |  | 1024/2048 | 1024/2048 |  | 
DSA |  | L:1024,N:160 | L:1024, N:160 |  | 
 |  | L:2048, N:224 | L:2048, N:224 |  | 
 |  | L:2048, N:256 | L:2048, N:256 |  | 
AES | ECB | 128/192/256 | 128/192/256 | 128/256 | 128/256
 | CBC | 128/192/256 | 128/192/256 | 128/256 | 128/256
 | CTR | 128/192/256 | 128/192/256 | 128/256 | 128/256
 | GCM | 128/192/256 | 128/192/256 | 128/256 | 
 | CCM | 128/192/256 | 128/192/256 |  | 
 | XTS | 128/192/256 | 128/192/256 |  | 
TDES | ECB | 168 | 168 |  | 
 | CBC | 168 | 168 |  | 
HASH | SHA1 | ✓ | ✓ |  | 
 | SHA256 | ✓ | ✓ |  | 
True Random Number Generator TRNG |  | ✓ | ✓ | ✓ | ✓
Identity (Asymmetrical)
Confidentiality (Symmetrical)
Integrity
Notes: The lower end SKU’s(S1, S3) only provided for symmetrical encryption (E.g. Confidentiality with shared secret keys) and the higher end SKU’s (S5, S7) provided for asymmetrical encryption (E.g. Trust and symmetrical encryption with temporary symmetrical keys).
Note that Identity functions consume the most power, but are done typically only periodically (e.g. once every few hours or once a day). However, in some applications they may occur more often.

## Slide 11: Security MPU
Provides regions that can only be accessed by “secure code”
Secure regions are protected from unauthorized accesses by:
    A non-secure program
    Masters, such as the DMA, DTC
    From debugger
Allows untrusted code to operate along side trusted code
The Setting is stored in Flash
The Security MPU is activated before fetching the reset vector
PC Region 0
CPU Bus
Bus of Master Group A,B,C
Monitor of Group A, B, C
Mask of access
Mask of Access
Mask of Access
PC Region 1
Memory Protection Units
Bus Master MPU
Security MPU
Bus Slave MPU
Region 0
Region 1
Region 0
Region 1
Region 2
PC Region 0
Region 1
Region 2
Region 3
Region 0
Region 1
Region 2
Region 3
Region 0
Region 1
Region 2
Region 3
Monitor of System Bus
Monitor of D Code Bus
Program Counter

## Slide 12: Flash Access Window
Write-protects an area within the User flash to prevent undesired self-programming
Area protection can be enabled only during self-programming in single-chip mode per block basis
Setting is stored in Option Flash
Once the lock bit (AWSC) is enabled, the setting is frozen
Flash Area Protection
Block 1
Block 2
Block 3
Block 5
Block 7
…
Block N
0x3FFF
0x4000
0x2000
0x1FFF
0x0000
End Block
Start Block
Accessible
Protected
Protected
Block 4
Block 6
Access Window
Block 0

## Slide 13: Protection by FAW and Security MPU
OTP & Protected from Non-Secure code(A)
    Define R/W access protection area
    Protected area cannot be accessible
    Suitable for secure boot loader and signature keys
Protected from Non-Secure code, Programable (B)
    The data in this region is protected from non-secure program
    However, it can be re-programmable
    It can be considered as secured programmable area
    Suitable for keys and secure program that need to be updated during the lifecycle
Application code, Programmable (C)
    Regular programmable area
    Suitable for Firmware application that can be updated in field
Flash
Access
Window
Security
MPU
Accessible
Programmable
Not accessible
Not programmable
Not accessible
Programmable
(C)
(A)
(B)
User Flash

## Slide 14: Wrapped Key Crypto API
SCE
Plain-text key
HRK
(Hidden Root Key)
Decrypted with HRK
Use Wrapped Key
Key Wrapped Key
Plain Text
Encrypted Text
Encrypt with plain key
SCE
RNG (Generate plain key)
Key Wrapped Key
HRK
(Hidden Root Key)
Encrypted with HRK
Generate Encrypted Key
AES Key Wrapping Interface APIs
    Generate key-wrapped AES key
    Encrypt data using key-wrapped AES key
    Decrypt data using key-wrapped AES key
RSA Key Wrapping Interface APIs
    Generate RSA key-pair, key-wrap private key
    Verify/Encrypt data using RSA public key
    Sign/Decrypt data using key-wrapped RSA private key
Wrapped Key can be stored in non secure storage
The wrapped key is only valid on the device that wrapped

## Slide 15: Key storage schemes
SCE
MPU Protected
Unprotected
Raw Key in protected memory
Raw Key is generated from TRNG
SCE wraps key with its unique key
Key Generation
Secure Key Injection

## Slide 16: Security components in synergy
Application
Synergy Microcontrollers
Synergy Software Package (SSP)
BSP
ThreadX®
RTOS
HAL Drivers
FileX®
GUIX™
USBX™
NetX™
NetX Duo™
Functional Libraries
Application Framework
Crypto Library
TLS
Microcontroller
    Secure Crypto Engine
    Security MPU(memory protection unit)
    Flash Access Window
Secure Boot Loader (Option)
    Maintain integrity of software on Microcontroller
    If updated firmware is pending, flash it securely
Crypto Library included in SSP
    High level API for using Crypto hardware accelerator
Security Protocol stack
    TLS
Firmware Update (Option)
    Download updated Firmware
Firmware Update
Secure Crypto Engine
Security MPU
Flash Access Window
Secure Boot Loader
Notes: A summary of items previously discussed. Also show the OS (e.g. ThreadX a real time operating system) and other related features (FileX, GUX, etc.)

## Slide 17
Security level planning

## Slide 18: Life cycle management
Update Firmware Server
OEM
Renesas
OEM
End Product
OEM
Application
Firmware
Secure
Boot loader
Bare MCU
End User
Contract Manufacturer

## Slide 19: Security challenges
Threat | Solution | Comments
Device Malware Device malfunction causing direct injury or damage “Backdoor” into networking causing injury or damage/loss | Secure Boot / Flash Ensure firmware is authentic, unmodified, and can’t be rolled back to a version with security vulnerabilities | Requires mastering tools (for OEM to sign and optionally encrypt firmware) and infrastructure for manufacturing Option: Most OEM’s also need infrastructure for securely updating firmware in the field
Device IP theft, Cloning, Vulnerability Analysis | Secure Boot / Flash + IP Protection Option | Requires additional infrastructure for encrypting individual keys for each device during manufacturing and field updates
Data-in-Motion (Device <-> Cloud) Spoofed identity Data is modified Data is replayed Eavesdropping or theft of data | TLS | Standard protocol which supports authentication of Cloud-By-Device and optionally Device-By-Cloud
Data-at-Rest (On Device) Application Specific Requirements: Protecting data when it’s on the device Encrypting/protection data before sending to cloud (e.g. encrypted for specific targets) Application specific protocols Other | Security Services / Toolbox Crypto API’s, TRNG, Secure Key Storage, reference examples | 
Cloud Connectivity
1The TLS Identity will not be issued unless the Secure Boot / Flash identity is validated. Or alternatively the Secure Boot / Flash identity is used as the TLS identity.

## Slide 20: Secure boot / flash firmware solution tiers
Security Tier |  | Integrity Validate firmware on flash and boot Firmware is authentic Not modified | Identity with Certificates Securely provisioned and stored Unique ID for each device allows: Attest/prove to the Cloud that the device is trusted Device-to-Cloud trusted communications (e.g. Chain-of-trust to TLS device identity) | IP Protection Firmware is encrypted by OEM and decrypted inside MCU target Firmware can only be flashed to selected number of devices (e.g. to prevent cloning/overproduction)
0 | No Security |  |  | 
1 | Secure Boot / Flash |  |  | 
2 | Trusted Device |  |  | 
3 | Trusted Device w/ IP Protection |  |  | 

## Slide 21: Tier 0 – No security
OEM Firmware Release Tools
MCU
Write protected
OTP @ Initial Flash
Read protected
Manufacturing Programming Center
Programmer
Data Center
FW Update Infrastructure
Cloud Operations
Physical
Cryptographic
None Required
Security

## Slide 22: Tier 1 – Secure Boot
OEM Firmware Release Tools
MCU
Write protected
OTP @ Initial Flash
Read protected
Programmer
Data Center
FW Update Infrastructure
Cloud Operations
Physical
Cryptographic
None Required
Security
Create OEM Secured Identity
Sec Boot Loader
Setup Boot Loader with OEM Identity used to validate releases
Manufacturing Programming Center
Sec Boot Loader
Firmware Signed with Private Key
Validates Firmware Signature

## Slide 23: Tier 2 – trusted device
OEM Firmware Release Tools
MCU
Write protected
OTP @ Initial Flash
Read protected
Data Center
FW Update Infrastructure
Cloud Operations
Physical
Cryptographic
None Required
Security
Manufacturing Programming Center
Sec Boot Loader
OEM ID
OEM Identity is created and provisioned to MCU
(Key Injection)
Option: Key Generation on Device1
2 Private key never leaves MCU. Key pair is generated on the MCU, the public key is sent to the Programmer and a certificate is issued and sent to the MCU
1 Hardware Security Module – Computing appliance platform w/ extremely high physical security & cryptographic speed
Cert Authority
(Typically hosted in an HSM1)
Issues cert
(Using public key provided by Programmer)
OEM ID
May be issued with local identity
Contains HSM1
Programmer
Sec Boot Loader
Cert Authority root certificate used to validate device identities
Cloud Cert Authority
Delegate
Centralized Cert Lifecycle Management Option
Expire / renew cert
Invalidate and/or authorize new delegate
Invalidate device cert manually (e.g. decommission device)
Analytics – detect compromised cert + cert invalidation and re-issuing
Can Issue certs only from Centralized OEM controlled facility
Or Centralized

## Slide 24: Tier 3 – trusted device + IP Protection
Contains HSM1
Option: Key Generation on Device1
OEM Firmware Release Tools
MCU
Write protected
OTP @ Initial Flash
Read protected
Data Center
FW Update Infrastructure
Cloud Operations
Manufacturing Programming Center
Sec Boot Loader
OEM ID
Cert Authority
(Typically hosted in an HSM1)
OEM ID
May be issued with local identity
Cloud Cert Authority
Delegate
Centralized Cert Lifecycle Management Option
Expire / renew cert
Invalidate and/or authorize new delegate
Invalidate device cert manually (e.g. decommission device)
Analytics – detect compromised cert + cert invalidation and re-issuing
Can Issue certs only from Centralized OEM controlled facility
Or Centralized
Programmer
Sec Boot Loader
FW Encryption Key
Physical
Cryptographic
None Required
Security
Encrypt firmware w/ key specific to release
Transfer Key which can be used limited # times
Key is encrypted for each MCU using its OEM ID
..and decrypted with assoc. private key
..which decrypts firmware
HSM
Similar implementation in update infrastructure is required, except counter not needed (i.e. an existing device can always be updated)
Secure code goes into secure memory1
1Only the portions of the code which access secure data (e.g. OEM ID, session keys) should go into secure memory (otherwise if all the code is in secure memory, any hack into the application could compromised the sensitive data)

## Slide 25
Secure boot loader
referrence project

## Slide 26: SECURITY Boot loader reference project
  Secure Boot Loader and tools that support Security Tier 3 level
  Example PC tools
      Secure Boot Loader Packaging tool
      Secure Boot Loader Installer tool
      Key DB
      Firmware Mastering tool
      1st Time Programming tool
      Deploy Update Firmware tool
  Example device code
      Secure Boot Loader
      Sample SSP application with firmware update
      Recovery manager
  User’s Guide

## Slide 27: Build secure boot loader
  Prepare Secure Boot Loader
      Generate Signature key
      Customize secure boot loader functionality if needed

## Slide 28: Device Personalization
  Program Secure Boot Loader
      Secure Boot loader and signature public key
      Device Certificate
  Enable protections
      Security MPU
      Flash Access Window
      JTAG ACCEDD ID (Disable JTAG port)
  After this personalization process, the device will accept only a binary image that is created by the Synergy Mastering tool
USB/UART convert cable
USB/UART convert cable
5V
Power supply
Log output
Download Secure Boot Loader

## Slide 29: Mastering firmware
  Generate UPK (Update Protection Key) and Save to Smartcard
      AES Encryption Key for the Firmware
      Signature Key for signing the Firmware
  Sign Firmware image
      Sign the Firmware by Signature key for the version 1.0
  Encrypt the Firmware by the AES Encryption Key
UPK

## Slide 30: Deploy firmware
USB/UART convert cable
USB/UART convert cable
5V
Power supply
UPK
  Authenticate Device
      Device sends Device Certificate to the Deploy tool on PC
      If successfully verified the Device Certificate, deploy tool encrypt UPK by Device Specific Encryption Key within the Device Certificate
  Transfer UPK and Firmware to Device
      Deploy tool transfer the encrypted UPK and encrypted Firmware to device
  Program the Firmware
      Security Boot Loader decrypt UPK and Firmware and Program decrypted Firmware within the Device

## Slide 31: Mastering firmware for update
  Generate UPK (Update Protection Key) and Save to Smartcard
      AES Encryption Key for the Firmware
      Signature Key for signing the Firmware
  Sign Firmware image
      Sign the Firmware by Signature key for the version 2.0
  Encrypt the Firmware by the AES Encryption Key
  Upload to Update Firmware server
UPK

## Slide 32: download firmware update
USB/UART convert cable
USB/UART convert cable
5V
Power supply
UPK
  Authenticate Device
      Device sends Device Certificate to the Deploy tool on PC
      If successfully verified the Device Certificate, deploy tool encrypt UPK by Device Specific Encryption Key within the Device Certificate
  Transfer UPK and Firmware to Device
      Deploy tool transfer the encrypted UPK and encrypted Firmware to device
  Program the Firmware
      Security Boot Loader decrypt UPK and Firmware and Program decrypted Firmware within the Device

## Slide 33
Implementation planning

## Slide 34: Implementation planning5
  Define security policy
      Identifies threats
      Identifies things to protect
      Risk assessment when the security is compromised
  Target Security Tier level
      Based on security policy, decide Security Tier level
  Design and Manufacturing process plan
      Tier 1 or above requires secure(trusted) process for design and manufacturing
      Tier 3 requires device unique key pair generation during the manufacturing, there is huge impact for manufacturing process
      Requires appropriate secure environment for design and manufacturing
  Memory map in MCU
      Secure Boot Loader area
      Application Firmware area
      Firmware download buffer for Pending image
      Healthy Firmware image back up

## Slide 35: Security policy planning template
 | Development | Manufacturing, Warehouse, Transporting | In use by user, Maintenances | Discard, End of life
What to protect |  |  |  | 
Threat |  |  |  | 
How to protect |  |  |  | 
Cloud Connectivity

## Slide 36: Security policy planning template – SAMPLE
 | Development | Manufacturing, Warehouse, Transporting | In use by user, Maintenances | Discard, End of life
What to protect | Firmware IP (Source code) Security assets (security keys, root of trust) | Firmware IP Root of trust Security assets Cloning | Firmware IP Root of trust Security assets End user information | Firmware IP Root of trust Security assets End user information
Threat | Unauthorized access External access Internal access | Unauthorized access External access Internal access Create Counterfeit product | Unauthorized access External access | Unauthorized access External access
How to protect |  |  |  | 
Cloud Connectivity

## Slide 37: planning for secure boot implementation
Check point | Answer
Is there any confidential data belongs to user during the period that user is using the product? If yes, what? | 
Is there any confidential data/program when you ship the product? If yes, what, who owns? | 
How long is the product’s life? | 
Is the product connected to other device or network? If yes, what, how? | 
Do you need to identify each individual product in the field to manage product’s functionality? | 
Do you deploy firmware update to the product in the field? | 
Do you host the firmware update distribution server in Cloud? | 
Is any 3rd party involved for application on the product or service? | 
Do you intend to host the private CA for your product? | 
Do you need TLS in application? | 
In event of the product detect malicious behavior, what is the reaction? | 
Cloud Connectivity

## Slide 38: planning for secure boot implementation
Check point | Answer
Is the software development team in one physical location? | 
Is the design site physically secure? Is there any access control? | 
Do you trust behavior of employees who have access to the design site? | 
Do you manufacture the product in trusted environment? | 
Do you trust behavior of employees who have access to the production facility? | 
Cloud Connectivity

## Slide 39
Secure Cloud Connectivity

## Slide 40: Secure IoT connection with Cloud
Basic building blocks of secure connectivity
Cloud Service
“Thing”
RESTful API
MQTT / TLS
Monitor and Control
Renesas Dashboard
Dashboard

## Slide 41: NetX Secure™
  Transport Layer Security - TLS v1.2
    Fundamental part of secure on-line communication. This is what your bank is using.
  Socket layer security with NetX Duo™
  Security 3 ways-
    Secrecy – TLS establishes secret keys between client & server using RSA and uses crypto algorithms for payload such as AES
    Integrity – Alteration or forgery of TCP packet content is detected using hashing algorithms such as SHA-1
    Authentication – Ensure data is communicated only to intended target. Prove identity of remote host by using digital certificates
  Initial TLS Handshake establishes ciphers & hashes for the session
  Once session is established, communication is accompanied by records that ensures integrity.
Notes: Everybody is talking about secure communication and there are very good reasons for that. So many companies with huge databanks have been hacked and data has been intercepted and decoded when not protected sufficiently. Renesas listened to customers and added TLS in the NetX Secure software. It is so important for our platform to offer secure on-line communication that Renesas decided to include TLS (and MQTT for that matter) in SSP 1.30.

## Slide 42: MQTT for NetX Duo™
  Message Queue Transport Telemetry (MQTT)
  Designed for lightweight M2M communications
    Memory constrained devices, typically MCUs
    Low-bandwidth, high-latency or unreliable networks
  Publish/Subscribe model – Perfect for IoT devices
    Publisher and subscriber do not need to know each other (by ip address and port for example)
    Publisher and subscriber do not need to run at the same time.
    Operations on both components are not halted during publish or receiving
Notes: MQTT is one of several options to connect sensors to the cloud. A so called MQTT-Broker receives data from a sensor. Data is stored in the cloud and ready for subscribers to be pulled from there. The communication is asynchronously and does not require a simultaneous on-state of sensor and client. The sensor can update the data on the broker when it changes or based on a certain timing pattern.

## Slide 43: Bringing it all together
TLS / MQTT for secure network communications between ‘things” and cloud
Wireless Application Frameworks in SSP for easy WiFi and Cellular implementation
A means to connect to major cloud service providers with no barrier to get started

## Slide 44: Synergy Enterprise Cloud Toolbox
RENESAS CONFIDENTIAL
Use Synergy MQTT & TLS to connect to cloud vendor of your choice
1
Quickly compare connectivity with Ethernet, Wi-Fi, and Cellular using Synergy Frameworks
2
Visualize sensor data in your own private web based Dashboard
3
Integrate your Dashboard account with your own cloud account
4
Use embedded and Dashboard code as starting point; modify for your own application
5
  Software delivered in a Synergy Application Project
    Name: Synergy Enterprise Cloud Toolbox
    ZIP file of App Note and code projects
  Software executes on PK-CLOUD1 kit
Connect in 10 minutes !
CAT3 Cellular
Sensor Shield
Synergy PK-S5D9 Kit
Wi-Fi
PK-CLOUD1

## Slide 45: Synergy enterprise cloud toolbox
Connect a Synergy kit
1
Choose an enterprise cloud service
2
Visualize data and control the kit with the Dashboard
3

## Slide 46: PK-Cloud1 Kit
Standard Synergy
PK-S5D9 Kit
WiFi Module (Pmod) -
Longsys GT-202 802.11 b/g/n with QCA4002 chipset
Cellular Modem (Pmod) - NimbeLink CAT3
Note: Cellular connectivity only supported for USA, Europe, and India
Sensor Shield (Arduino)
GPS
Gyroscope
Accelerometer
Temperature
Humidity
Pressure
Contact your local Renesas sales representative to inquire about receiving a PK-CLOUD1 kit

## Slide 47: system architecture Synergy Enterprise Cloud Toolbox
On Dashboard, the user can:
Create an account
Select Enterprise Cloud Service (AWS, Azure, or Google Platform)
Associate kit with account
Determine if kit is online
Monitor sensor data from kit and control kit functions
* Google Cloud support to be added in October 2017
Enterprise Cloud
Amazon Web Service,
Microsoft Azure, Google Platform*
RESTful API
TLS / MQTT
PK-CLOUD1
Monitor and Control
Renesas Dashboard
Renesas-hosted Dashboard
Master accounts - user does not have access
User-created accounts
USB
CLI
Command Line user Interface (CLI), the user can:
Provision a kit (get the ID, register an email address)
Provision connectivity type (Ethernet, Wi-Fi, CAT3)

## Slide 48: Dashboard features
Move PK-CLOUD1 Kit and watch accelerometer readings change
“Thing” to Cloud
Change selections on Dashboard and watch LEDs turn on/off on the PK-CLOUD1 Kit
Cloud to “Thing”

## Slide 49: Go from demo to application
Synergy Enterprise Cloud Toolbox Application Project contains:
Synergy SSP project (e2studio and IAR) with C source code
Dashboard with Java/JavaScript source code
Quick Start Guide
Application Note
Download the Application Project from:
www.renesas.com/cloudtoolbox
Use source code as starting place to connect to your own cloud account and add features needed for your application
Download
Synergy Enterprise Cloud Toolbox
S5 Series MCUs
Renesas Synergy Tools & Kits
Renesas Synergy Promotion Kit PK-CLOUD1
Application Note, Sample Programs (e2 studio and IAR ENSYN) are included
Synergy Enterprise Toolbox – Application Project
an-synergy-enterprise-cloud-toolbox.zip

## Slide 50
Summary

## Slide 51: Renesas Synergy Security solution
Availability
Integrity
Confidentiality
  Security Hardware Resources
      SCE
      Memory protections
  Security Software Resources
      Crypto Library
      Secure Boot Loader and Mastering tools
      Secure communication stack (TLS)
  Ecosystem partners
      Arrow and Avnet for Secure Programming Service
      Secure Thingz and Data I/O for Secure Programming equipment
      Digicert, Global Sign for Certificate Authority